## Slide 1: V3DJoint
Measurement of the Quality Factor of flexible joints
Alessandro Mazza, Danilo Ricciardella, Victor Sanz Sanchis, Davide Quaranta
Phys. Lab II - Mid Term Report
05/05/23

## Slide 2: Why Flexible Joints?
Elastic joints are often used in experiment to build sensors
  Accelerometers
  Displacement sensors
  Tiltmeters etc…
In particular, in a GW detector thermal noise is important and can be reduced by lowering the temperature of the suspended mirrors
Therefore performing joints at cryogenic temperatures are needed
Goal :
  Testing performance of 3D printed metal joints
  Comparing with standard production techniques

## Slide 3: Why Flexible Joints?
Aluminum-Silicon-Magnesium (AlSi10Mg)
CuCrZr and AlSi10Mg
Copper-Chromium-Zirconium (CuCrZr)
3D Printed
Electroerosion
Tested
To be Tested
To be Tested

## Slide 4: Theoretical model
The joint acts like a damped harmonic oscillator and has the following differential equation:
Finding the expression for the position and the velocity, the energy stored in one oscillation can be calculated:
The oscillation is governed by the angular frequency ⍵ and one cycle is completed in a period T = 2𝜋/𝜔, so the energy lost per cycle
Now the quality factor (Q) can defined as 2π times the ratio of the energy stored in one oscillation over the energy lost in a cycle:

## Slide 5: Experimental Setup & Procedure
Bring the chamber to a certain T with the help of a cryocooler Pulse Tube
Kick the balance by sending a current through the magnet
Measuring displacement with laser sensor
Fourier Transform through Spectrum analyzer
Measure the decay time of first harmonic
Fit to find 𝜏
Compute Q
x(t) = Ae-t/𝜏cos(𝜔t + 𝜑) → Q = 𝜋𝜏𝑓

## Slide 6: Experimental Setup & Procedure
Observing the amplitude decay we’re able to extrapolate 𝞽 and calculate
Oscillation amplitude decay for f=1.5Hz at T=241.8K
Sample: Copper-Chromium-Zirconium (3D printed)
Oscillation amplitude decay for f=1.563 Hz at T=10.6K
PLOT QVST

## Slide 10: Consideration (?)

## Slide 11: Experimental setup
Pulse tube crycooler connected to a helium compressor;
Fiber bundle;
Thermometer;
Coil and magnet;
Generator;
Signal analyzer;

## Slide 12
Alluminum-Silicon-Magnesium alloy (AlSi10Mg) Samples
Copper-Chromium-Zirconium alloy (CuCrZr) Samples
CuCrZr and
AlSi10Mg
samples also produced by electroerosion (standard process) at Virgo for comparison with 3D printed samples